## Slide 1: How do we Improve the Efficiency of the Present Solar Systems? Is 29% Max Efficiency an Acceptable Max
By Abubakar Audu

## Slide 2: Construction Improvements
Buried Contacts 1. In solar cells construction, instead of the top contacts lying across the surface and blocking sunlight, the cells contacts can be buried into grooves down the surface. These grooves can be made by using a laser to blast on to the surface of the silicon wafers. There is no extra cost incurred. The efficiency to the range of 16-18%

## Slide 3: Construction Improvements
Ribbon Substrates
2. In silicon wafer construction, a cylindrical ingot of silicon is made and is then sliced into wafers.
One better way to improve this is to use ribbon substances. In this technique, molten silicon rises up between rectangular faces of a carbon die.
Same material hence more economical way.

## Slide 4: Construction Improvements
3. Thin Film
It is better to deposit the thin layer of the photoactive material on to a supporting layer. This will reduce the amount of the semi- conductor used and will make possible the construction of a cell with a larger area.
One drawback to this technique is that the supporting layer might be too expensive for small scale production. In large scale production, the costs of manufacturing thin- film cells will approach those of the materials used.

## Slide 5: Construction Improvements
4. Mixture of Substances
    A mixture of silicon and germanium can be used to convert the blue, green and the red wavelengths of sunlight. In this build up, stacks of cells, each targeting a particular wavelength of light is constructed.
    One of such promising mixture is the mixture of cadmium and tellurium to form cadmium telluride (CdTe). Other considerable mixtures are CuInSe2, TiO2 among others.

## Slide 6: Construction Improvements
5. Sun Tracking

## Slide 7: Taking a Look at the Theoretical Maximum
Presently, the theoretical maximum efficiency of solar energy is 29%. What happens to the other 71%? Using our understanding of p-n junction semi-conductors, we will better understand what is going on.

## Slide 8: Taking a Look at the Theoretical Maximum
The sunlight striking the earth’s atmosphere carries about 1.35 KW of energy per square meter. By the time this light reaches the surface of the earth, it carries about 1 kW/m2. The photons which make up this light have a range of different energies. The majority of the lost is caused by the energy of the photons being spread out
E = nhf where n = 1,2,3……. h = Planck’s constant = 6.63 *10-23 Js

## Slide 9: Taking a Look at the Theoretical Maximum
The perfect photon would have an energy exactly equal to the band gap of silicon.
A photon with less energy than the band gap will waste 24% of the solar energy.
If a photon has an energy larger than the band gap, the excess energy is not used. This causes an additional loss of 32% of the solar energy.

## Slide 10: Proposed Solutions to the Theoretical Maximum Problem
Instead of using only silicon, using stochastic processes, we can design a system where silicon and other semi-conductive materials are randomly placed next to each other. In this system with favorable probabilistic occurrence, more of the photons that are too small for silicon will fall on a semi-conductive material with smaller band gap than those with higher band gap. The same is true for the photon with higher energy

## Slide 11: Proposed Solutions to the Theoretical Maximum Problem
Reflection: means photons bouncing off the crystal instead of going into the crystal. Better coating of the surface of the cells can increase the efficiency by 3%.
Impurities: Purer crystal with a better trade off between cost and efficiency should be used.